## Slide 1
CAPSTONE 2 — AI-Assisted Arduino/ESP32
Code Generation and Verification
How reliable is AI-generated embedded code, and what verification process
makes it safe to use?
Three AI tools compared: ChatGPT • Claude • Gemini
Five beginner tasks on Arduino Uno (Wokwi simulation)
ECE AI Capstone Projects • Final Demo

## Slide 2
Methodology — The 12 Steps
From task selection to final demo
2 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
▪ Selected 5 beginner tasks: LED blink · DHT11 temp/humidity · HC-SR04 distance · Servo sweep · I2C LCD
▪ Wrote baseline vs improved prompts (role, board, pins, libraries, constraints) for each task
▪ Generated code with 3 AI tools: ChatGPT, Claude, Gemini
▪ Compiled & simulated each program in Wokwi (Arduino Uno)
▪ Logged compile errors, wrong pins, missing libraries, logic errors
▪ Applied human fixes; noted which fixes AI could / could not suggest
▪ Scored tools with a weighted rubric; compared baseline vs improved prompts
▪ Documented all prompts and versions on GitHub
▪ Produced coding guide, safety/licensing notes, and this presentation

## Slide 3
Three AI Tools, Same Five Tasks
Tool attribution taken from each bundle's diagram.json
3 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
AI Tool | Bundle (zip) | author tag | Strength | Weakness / risk
ChatGPT (OpenAI) | wokwi_beginner_tasks.zip | OpenAI | Clean, minimal code | Less documentation
Claude | wokwi_beginner_embedded_tasks.zip | Beginner Embedded Guide | Most complete; best error handling | Slightly verbose
Gemini | wokwi_capstone2_projects.zip | capstone | Fast, concise output | Missing library dep; redundant wiring
Sample comparison — Task 1 LED Blink:
ChatGPT/Claude: external LED on D8 + 220 Ω resistor, 1 s interval.
Gemini: uses D13 (Arduino's built-in LED pin) but still adds an external LED + resistor — redundant wiring.

## Slide 4
Verification: Errors Found & Human Fixes
What was wrong with the AI-generated code
4 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
# | Task | AI Tool | Error type | Details | Human fix
1 | LED blink | Gemini | Wrong wiring | Uses D13 (built-in LED) + redundant external LED + resistor | Rewired external LED to D8
2 | DHT temp/humidity | Gemini | Missing library | libraries.txt lists only "DHT sensor library"; needs Adafruit Unified Sensor too | Added Adafruit Unified Sensor
3 | DHT (all tools) | All three | Sim vs hardware | Wokwi uses wokwi-dht22 part; physical DHT11 needs DHTTYPE DHT11 | Added explicit code/README note
Key takeaway:
AI could suggest surface fixes (pin numbers, comments) when prompted, but could not reliably detect missing library dependencies
or hardware/simulation mismatches on its own. Human domain knowledge was required for all three fixes.

## Slide 5
Tool Comparison — Scoring Rubric
Weighted rubric 0–5 across 6 criteria, all 5 tasks
5 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
Criterion | Weight | ChatGPT | Claude | Gemini
Code correctness | 25% | 5 | 5 | 4
Wiring accuracy | 20% | 5 | 5 | 3
Library completeness | 15% | 5 | 5 | 3
Documentation | 15% | 4 | 5 | 3
Error handling | 10% | 4 | 5 | 3
Prompt follow-through | 15% | 4 | 5 | 3
Weighted total | 100% | 4.55 | 4.85 | 3.45
Finding:
Improved prompts (role / board / pins / libraries / constraints) significantly outperform baseline prompts across all tools.
Claude scored highest; Gemini needed the most human fixes.

## Slide 6
Coding Guide & Safety
How to prompt for embedded code + risks to manage
6 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
6-Part Prompt Template
▪ Role — embedded systems engineer/instructor
▪ Board — e.g. Arduino Uno
▪ Task — sensor/actuator, pins, behavior, interval
▪ Libraries — exact names or built-in only
▪ Constraints — baud rate, error handling, Wokwi parts
▪ Output format — sketch.ino, diagram.json, libraries.txt
Safety & Licensing
▪ Review sketch pins against diagram.json before powering real hardware
▪ Install all libraries incl. transitive deps (e.g. Adafruit Unified Sensor)
▪ Note simulation-vs-hardware differences (DHT11 vs DHT22)
▪ AI-generated code copyright status is uncertain
▪ Review tool Terms of Service before commercial use
▪ Add LICENSE file + library attribution on GitHub

## Slide 7
Conclusion & Recommendation
Is AI-generated embedded code safe to use?
7 / 7
CAPSTONE 2 — AI-Assisted Arduino/ESP32 Code Generation & Verification
ECE AI Capstone Projects
AI is a strong DRAFTER
NOT a reliable verifier
Human review required
Recommendation:
▪ Use AI to generate starter embedded code (fast, covers all 5 tasks)
▪ Then compile, simulate in Wokwi, review wiring against datasheets
▪ Install all libraries; test on real hardware with current-limited supply
▪ Document all prompts, versions, errors, and fixes on GitHub
▪ Only deploy after human verification — never trust AI output blindly